## Slide 1: Built-in self-test of logic blocks in FPGAs (Finally, a free lunch: BIST without overhead!)
ECE 7502 Class Discussion
Seyi Ayorinde
Tuesday, February 3rd, 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Post Silicon Verification
Test
Test

## Slide 3: Built-In Self Test (BIST)
Allows chips to test themselves
Purpose: reduce cost of testing
  Reduce test cycle duration
  Reduce complexity of test/probe setup
  Reduced cost of expensive automatic test equipment (ATE)

## Slide 4
http://www.ece.uc.edu/~wjone/BIST2.pdf

## Slide 5: Field Programmable Gate Arrays (FPGAs)
Reconfigurable integrated circuits (ICs)
Collection of look-up tables (LUTs) connected by reconfigurable interconnect
Distributed SRAM bitcells control interconnect and logic in LUTs
LUTs are grouped together into programmable logic blocks (PLBs)

## Slide 6: FPGA Fabric
http://www.fpga-site.com/faq.html

## Slide 7: Challenges for FPGA Testing
More coverage needed than traditional IC testing
  Multiple configurations
  Current solution – configure several applications
Non-classical fault types
  Interconnect faults
  Configuration faults
Additional Development effort is required for on-board and system-level testing

## Slide 8: BIST for FPGAs – FREE LUNCH!!
Programming logic blocks as TPGs and ORAs for other PLBs
  Pseudoexhaustive Test Technique
Allows for complete testing for all logic blocks
Allows testing at-speed
BIST incurs no overhead
  Logic blocks can be reconfigured for target functionality, BIST structures “disappear”

## Slide 9: Approach
TPGs – exhaustive test patterns
  Binary counters
Blocks under test (BUTs)
  18 inputs, 4 outputs
  Need 5 TPGs for standard PLB
ORAs compare outputs from BUTs to expected outputs
  Each ORA can compare a maximum of 4 BUTs
  5th LUT input turns off ORA once an error is found
Approach can be extended to many FPGA architectures
  Table shows other configurations
  This paper – AT&T ORCA
[1] Stroud et al, VTS’96

## Slide 10: Approach
Found total number of possible faults
  Used Fault Simulator to determine total # of possible faults
  1538 LUT faults + 440 FF faults + 246 Mux faults = 2224 total
9 Configurations needed
  Four LUT modes (RAM, Fast-Adder, 5-variable, 4-variable)
  5 FF options (combinations described in table 4)
[1] Stroud et al, VTS’96

## Slide 11: Results
18 total configurations needed
  9 catches 100% of faults for 87% of logic blocks
  Current ORCA manufacturing test
  Adds up to 1 sec of testing time to test all PLBs
[1] Stroud et al, VTS’96

## Slide 12: Limitations
Routing limitations
  Routing resources of target FPGA couldn’t support complete exhaustive testing
    Solution – only use inputs/outputs for the given test
Invisible logic
  When configurations are represented as gates, certain possibilities for testing are removed
    Solution – attempt to recreate missing circuits and overlay them
[1] Stroud et al, VTS’96

## Slide 13: Limitations
Lack of detailed configuration control
  Can’t make sure that each input of the output mux (for example) will be exercised, because CAD tools don’t give that type of control
    Solution – modify intermediate files or final configuration bit stream

## Slide 14: Conclusions
FPGAs could theoretically be fully tested without the need for any DFT circuitry by configuring PLBs in the FPGA as TPGs and ORAs for other PLBs
For the AT&T ORCA FPGA, 9 configurations can result in 100% fault coverage for a given PLB
18 total configurations for testing all PLBs (reduction from 32 configurations)
CAD tools made for FPGAs limit implementation

## Slide 15: Interesting Extensions
Menon et al, TCAD’06 [2] – Design specific path delay testing in LUT-based FPGAs
  Testing delays of interconnect paths
Zhang et al, APCCAS’08 [3] – BIST approach for testing configurable logic and memory resources in FPGAs
  Using hard-macro (physical-macro library provided by Xilinx) for added control over LUT and block RAM resources
Rehman et al, DFT’13 [4] – BIST for logic and local interconnect resources in a novel mesh of cluster FPGA
  Compares BIST in tree-based interconnects to standard 2-D interconnects

## Slide 16: Self-heating Thermal-aware testing of FPGAs
Problem – Thermal testing is expensive and unreliable
  Expensive -> thermal chambers, time
  Unreliable -> low control
Solution – Configure logic blocks in the FPGA as heating elements to locally heat the FPGA in certain areas, removing the need for external temperature control

## Slide 17: Approach
Configure LUTs as self-heating-elements (SHEs)
  Series of toggling elements
  SHEs can then be distributed across the chip for uniform temperature control
[5] Amouri et al, DFT’13

## Slide 18: Approach
SHEs can also be used to provide gradient thermal profiles
[5] Amouri et al, DFT’13

## Slide 19: Results
Tested Virtex-5 FPGA
Thermal accuracy - ±1°C
Power Consumption – up to 14 W from normal 2.5 W
BIST configurations increases from 12 to 18
Chip temperatures ranging from 50-125°C
NO EXTERNAL TEMPERATURE SOURCE at the cost of longer testing times
[5] Amouri et al, DFT’13

## Slide 20: Discussion questions
Why are exhaustive RAM tests impractical?
In what way is figure 2 somewhat misleading?
Can we think of any possible ways to reduce the number of logic blocks necessary for TPGs?
What are the limitations to the manner in which the results are reported?
What other novel BIST structures (like self-heating) can we come up with?

## Slide 21: Papers
Stroud, C.; Konala, S.; Ping Chen; Abramovici, M., "Built-in self-test of logic blocks in FPGAs (Finally, a free lunch: BIST without overhead!)," VLSI Test Symposium, 1996., Proceedings of 14th , vol., no., pp.387,392, 28 Apr-1 May 1996
Menon, P.R.; Weifeng Xu; Tessier, R., "Design-specific path delay testing in lookup-table-based FPGAs," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on , vol.25, no.5, pp.867,877, May 2006
Zhiquan Zhang; Zhiping Wen; Lei Chen; Tao Zhou; Fan Zhang, "BIST approach for testing configurable logic and memory resources in FPGAs," Circuits and Systems, 2008. APCCAS 2008. IEEE Asia Pacific Conference on , vol., no., pp.1767,1770, Nov. 30 2008-Dec. 3 2008
Rehman, S.-U.; Benabdenbi, M.; Anghel, L., "BIST for logic and local interconnect resources in a novel mesh of cluster FPGA," Defect and Fault Tolerance in VLSI and Nanotechnology Systems (DFT), 2013 IEEE International Symposium on , vol., no., pp.296,301, 2-4 Oct. 2013
Amouri, A.; Hepp, J.; Tahoori, M., "Self-heating thermal-aware testing of FPGAs," VLSI Test Symposium (VTS), 2014 IEEE 32nd , vol., no., pp.1,6, 13-17 April 2014

## Slide 22: Paper Map
[1] Lin, D.; …"Effective Post-Silicon Validation of …," ICASICS’14.
[2] Oh, N.; …"Control-flow checking by software …," ITR’02.
[3] Das, P.; …"Gate delay modeling for pre- and …," ICCD’13.
[4] Keshava, J.; … "Post-silicon validation challenges: …” DAC’10.
[5] Mitra, S.; … "Post-silicon validation …," DAC’10.
[1] Proposed BIST structures for FPGA logic blocks
[2] BIST for FPGA interconnect
[4] BIST with novel FPGA arch.
[5] Self-heating Thermal Aware FPGAs
Addresses interconnect challenge
Addresses CAD issue
Uses different architecture, requires new approach
[3] BIST for FPGA using hard-macro
Expands design space for BIST in FPGAs to new axes

## Slide 23: Glossary
BIST: built-in self test
TPG: test pattern generator
ORA: Output response analyzer
FPGA: Field Programmable Gate Array
LUT: Look-up Table
PLB: Programmable Logic Block
SHE: Self-heating elements